## Slide 1
Network Classes and Subnetting
Lecture 31-33 (Theory)
Department of Computer Science and Engineering,
Chitkara University, Punjab
Computer Networks

## Slide 2
Index
2
1. Logical Addressing
2. Classful Addressing
3. Hierarchy of IPv4 Addresses
4. Network Classes (A,B,C,D,E)
5. Subnetting
Computer Networks

## Slide 3: Logical Addressing
Network Addressing is one of the major responsibilities of the network layer.
Network addresses are always logical, i.e., software-based addresses.
A host is also known as end system that has one link to the network. The boundary between the host and link is known as an interface. Therefore, the host can have only one interface.
A router is different from the host in that it has two or more links that connect to it. The boundary between the router and link is known as an interface, and the router can have multiple interfaces, one for each of its links. Each interface is capable of sending and receiving the IP packets, so IP requires each interface to have an address.
Each IP address is 32 bits long, and they are represented in the form of "dot-decimal notation" where each byte is written in the decimal form, and they are separated by the period. An IP address would look like 193.32.216.9 where 193 represents the decimal notation of first 8 bits of an address, 32 represents the decimal notation of second 8 bits of an address, and so on.
3
Computer Networks

## Slide 4: Logical Addressing (contd.)
4
Figure 1: Router and IP Addressing
Computer Networks

## Slide 5: Logical Addressing (contd.)
In the Figure 1, a router has three interfaces labeled as 1, 2 & 3 and each router interface contains its own IP address.
Each host contains its own interface and IP address.
All the interfaces attached to the LAN 1 is having an IP address in the form of 223.1.1.xxx, and the interfaces attached to the LAN 2 and LAN 3 have an IP address in the form of 223.1.2.xxx and 223.1.3.xxx respectively.
Each IP address consists of two parts. The first part (first three bytes in IP address) specifies the network and second part (last byte of an IP address) specifies the host in the network.
5
Computer Networks

## Slide 6: Classful Addressing
An IP address is 32-bit long. An IP address is divided into sub-classes:
Class A
Class B
Class C
Class D
Class E
An IP address is divided into two parts:
Network ID: It represents the number of networks.
Host ID: It represents the number of hosts.
6
Computer Networks

## Slide 7: In the diagram, we observe that each class have a specific range of IP addresses. The class of IP address is used to determine the number of bits used in a class and number of networks and hosts available in the class.
7
Figure 2: Classful Addressing
Computer Networks
Classful Addressing (contd.)

## Slide 8
8
Figure 3: Finding the classes in binary and dotted-decimal notation
Computer Networks

## Slide 9
IPv4 ADDRESSES
An IPv4 address is a 32-bit address that uniquely and universally defines the connection of a device (for example, a computer or a router) to the Internet.
An address space is the total number of addresses used by the protocol.
The address space of IPv4 is 232 or 4,294,967,296 (more than 4 billion).
If a device operating at the network layer has m connections to the internet, it needs to have m addresses. E.g.: router
9
Computer Networks

## Slide 10
10
Figure 4: Dotted-decimal notation and binary notation for an IPv4 address
Computer Networks
IPv4 ADDRESSES (contd.)

## Slide 11
Change the following IPv4 addresses from dotted-decimal notation to binary notation.
Solution
We replace each decimal number with its binary equivalent.
Example
11
Computer Networks

## Slide 12: Class A
In Class A, an IP address is assigned to those networks that contain a large number of hosts.
The network ID is 8 bits long.
The host ID is 24 bits long.
In Class A, the first bit in higher order bits of the first octet is always set to 0 and the remaining 7 bits determine the network ID. The 24 bits determine the host ID in any network.
The total number of networks in Class A = 27 = 128 network address
The total number of hosts in Class A = 224 - 2 = 16,777,214 host address
12
Computer Networks

## Slide 13: Class B
In Class B, an IP address is assigned to those networks that range from small-sized to large-sized networks.
The Network ID is 16 bits long.
The Host ID is 16 bits long.
In Class B, the higher order bits of the first octet is always set to 10, and the remaining14 bits determine the network ID. The other 16 bits determine the Host ID.
The total number of networks in Class B = 214 = 16384 network address
The total number of hosts in Class B = 216 - 2 = 65534 host address
13
Computer Networks

## Slide 14: Class C
In Class C, an IP address is assigned to only small-sized networks.
The Network ID is 24 bits long.
The host ID is 8 bits long.
In Class C, the higher order bits of the first octet is always set to 110, and the remaining 21 bits determine the network ID. The 8 bits of the host ID determine the host in a network.
The total number of networks = 221 = 2097152 network address
The total number of hosts = 28 - 2 = 254 host address
14
Computer Networks

## Slide 15: Class D
In Class D, an IP address is reserved for multicast addresses. It does not possess subnetting.
The higher order bits of the first octet is always set to 1110, and the remaining bits determines the host ID in any network.
15
Computer Networks

## Slide 16: Class E
In Class E, an IP address is used for the future use or for the research and development purposes. It does not possess any subnetting. The higher order bits of the first octet is always set to 1111, and the remaining bits determines the host ID in any network.
16
Computer Networks

## Slide 17
A block in class A address is too large for almost any organization. It means that most of the IP addresses in class A were wasted.
A block in class B is also very large.
A block in class C is probably too small for many organizations.
Class D addresses were designed for multicasting. Each IP address in this class is used to define one group of hosts on the Internet. The Internet authorities wrongly predicted a need of 268,435,456 groups. This never happened and many IP addresses were wasted.
Class E IP addresses were reserved for future use; only a few were used, resulting in another waste of IP addresses
17
Computer Networks

## Slide 18
Two level hierarchy in an
IPv4 address
Leftmost n bits (prefix) define the network id and,
The right most 32-n (suffix) bits define the host id.
The prefix is common to all devices in the network, suffix changes from one device to another.
18
Computer Networks

## Slide 19
Netid and Hostid:
This concept does not apply to class D and E.
For class A, one byte defines netid, and three bytes define hostid.
In class B, two bytes define the netid, and two bytes define the hostid.
In class C, three bytes define the netid , and one byte defines the hostid.
19
Computer Networks

## Slide 20
Mask:
The concept does not apply to classes D and E.
The mask can help us find netid and hostid.
The last column shows the mask in the form /n, where n can be 8,16, or 24. This notation is called slash notation or Classless Interdomain Routing (CIDR) notation.
20
Figure 5: Default masks for classful addressing
Computer Networks

## Slide 21: Rules for assigning Host ID:
The Host ID is used to determine the host within any network. The Host ID is assigned based on the following rules:
The Host ID must be unique within any network.
The Host ID in which all the bits are set to 0 cannot be assigned as it is used to represent the network ID of the IP address.
The Host ID in which all the bits are set to 1 cannot be assigned as it is reserved for the multicast address.
21
Computer Networks

## Slide 22: Rules for assigning Network ID:
If the hosts are located within the same local network, then they are assigned with the same network ID. The following are the rules for assigning Network ID:
The network ID cannot start with 127 as 127 is used by Class A.
The Network ID in which all the bits are set to 0 cannot be assigned as it is used to specify a particular host on the local network.
The Network ID in which all the bits are set to 1 cannot be assigned as it is reserved for the multicast address.
22
Computer Networks

## Slide 23
23
Figure 6: Number of blocks and block size in classful IPv4 addressing
Computer Networks

## Slide 24
Class | Higher bits | NET ID bits | HOST ID bits | No.of networks | No.of hosts per network | Range
A | 0 | 8 | 24 | 27 | 224 | 0.0.0.0 to 127.255.255.255
B | 10 | 16 | 16 | 214 | 216 | 128.0.0.0 to 191.255.255.255
C | 110 | 24 | 8 | 221 | 28 | 192.0.0.0 to 223.255.255.255
D | 1110 | Not defined | Not defined | Not defined | Not defined | 224.0.0.0 to 239.255.255.255
E | 1111 | Not defined | Not defined | Not defined | Not defined | 240.0.0.0 to 255.255.255.255
24
Computer Networks

## Slide 25
To overcome address depletion and give Internet access to more organizations, classless addressing was designed and implemented.
In this scheme, there are no classes but the addresses are still granted in blocks.
Classless Addressing
25
Computer Networks

## Slide 26
If an organization was granted a large block in class A or B, it could divide the addresses into several contiguous groups and assign each group to smaller networks (called subnets).
Subnetting increases the number of 1s in the mask.
26
Subnetting
Computer Networks

## Slide 27
The size of a class C block with a maximum number of 256 addresses did not satisfy the needs of most organizations.
In supernetting, an organization can combine several class C blocks to create a larger range of addresses.
In other words, several networks are combined to create a supernetwork or supernet.
E.g. an organization that needs 1000 addresses can be granted four contiguous class C blocks.
Supernetting decreases the number of 1s in the mask.
E.g. if an orgainzation is given four class C blocks, the mask changes from /24 to /22.
Classless addressing eliminated the need for supernetting.
27
Supernetting
Computer Networks

## Slide 28
In classless addressing, when an entity small or large, needs to be connected to the Internet, it is granted a block of addresses. The size of the block varies based on the need of the organization.
Address Blocks
Restriction-
The addresses in a block must be contiguous.
The no of addresses in a block must be a power of 2.
The first address must be evenly divisible by the number of addresses.
28
Computer Networks

## Slide 29
Figure (on next slide) shows a block of addresses, in both binary and dotted-decimal notation, granted to a small business that needs 16 addresses.
We can see that the restrictions are applied to this block. The addresses are contiguous.
The number of addresses is a power of 2 (16 = 24), and the first address is divisible by 16.
The first address, when converted to a decimal number, is 3,440,387,360, which when divided by 16 results in 215,024,210.
Example
29
Computer Networks

## Slide 30
30
Figure 7: A block of 16 addresses granted to a small organization
Computer Networks
Example (contd.)

## Slide 31
In IPv4 addressing, a block of addresses can be defined as
x.y.z.t /n
in which x.y.z.t defines one of the addresses and the /n defines the mask.
31
Computer Networks

## Slide 32
The first address in the block can be found by setting the rightmost 32 − n bits to 0s.
32
Computer Networks

## Slide 33
A block of addresses is granted to a small organization. We know that one of the addresses is 205.16.37.39/28. What is the first address in the block?
Solution
The binary representation of the given address is
11001101 00010000 00100101 00100111
If we set 32−28 rightmost bits to 0, we get
11001101 00010000 00100101 0010000
or 205.16.37.32
Example
33
Computer Networks

## Slide 34
Network Address:
The first address is called the network address and defines the organization network
First address is used as the network address that represents the organization to the rest of the world.
34
Computer Networks

## Slide 35
The last address in the block can be found by setting the rightmost 32 − n bits to 1s.
35
Computer Networks

## Slide 36
A block of addresses is granted to a small organization. We know that one of the addresses is 205.16.37.39/28. What is the last address in the block?
Solution
The binary representation of the given address is
11001101 00010000 00100101 00100111
If we set 32 − 28 rightmost bits to 1, we get
11001101 00010000 00100101 00101111
or
205.16.37.47
Example
36
Computer Networks

## Slide 37
The number of addresses in the block can be found by using the formula 232−n.
37
Computer Networks

## Slide 38
An organization that is granted a large block of addresses may want to create clusters of networks (subnets) and divide the addresses between the different subnets.
The rest of the world still sees the organization as one entity; however internally there are several subnets.
All messages are sent to the router that connects the organization to the rest of the Internet; the router routes the message to the appropriate subnets.
The organization has its own mask and each subnet must also have its own.
Three level of Hierarchy: subnetting
38
Computer Networks

## Slide 39
Suppose an organization is given the block 17.12.40.0/26, which contains 64 IP addresses. The organization has three offices and needs to divide the addresses into three subblocks of 32,16, and 16 IP addresses.
We can find the new masks as
Suppose the mask for the first subnet is n1 then 232-n1 must be 32, which means n1=27.
Suppose the mask for the second subnet is n2 then 232-n2 must be 16, which means n1=28.
Suppose the mask for the third subnet is n3 then 232-n3 must be 16, which means n1=28.
Example
39
Computer Networks

## Slide 40
40
Figure 8: Configuration and addresses in a subnetted network
Computer Networks
Example (contd.)

## Slide 41
Three-level hierarchy in an
IPv4 address
41
Figure 9: Three-level hierarchy in an IPv4 address
Computer Networks

## Slide 42
An ISP is granted a block of addresses starting with 190.100.0.0/16 (65,536 addresses). The ISP needs to distribute these addresses to three groups of customers as follows:
a. The first group has 64 customers; each needs 256 addresses.
b. The second group has 128 customers; each needs 128 addresses.
c. The third group has 128 customers; each needs 64 addresses.
Design the subblocks and find out how many addresses are still available after these allocations.
Example
42
Computer Networks

## Slide 43
Solution
Group 1
For this group, each customer needs 256 addresses. This means that 8 (log2 256) bits are needed to define each host. The prefix length is then 32 − 8 = 24. The addresses are
43
Example (contd.)

## Slide 44
Group 2
For this group, each customer needs 128 addresses. This means that 7 (log2 128) bits are needed to define each host. The prefix length is then 32 − 7 = 25. The addresses are
44
Example (contd.)

## Slide 45
Group 3
For this group, each customer needs 64 addresses. This means that 6 (log264) bits are needed to each host. The prefix length is then 32 − 6 = 26. The addresses are
Number of granted addresses to the ISP: 65,536
Number of allocated addresses by the ISP: 40,960
Number of available addresses: 24,576
45
Example (contd.)

## Slide 46
46
Figure 10: An example of address allocation and distribution by an ISP
Example (contd.)

## Slide 47
Change the following IPv4 addresses from binary notation to dotted-decimal notation.
47
Practice Questions

## Slide 48
Find the error, if any, in the following IPv4 addresses.
48
Practice Questions

## Slide 49
Find the class of each address.
a. 00000001 00001011 00001011 11101111
b. 11000001 10000011 00011011 11111111
c. 14.23.120.8
d. 252.5.15.111
Practice Questions
49

## Slide 50
A block of addresses is granted to a small organization. We know that one of the addresses is 205.16.37.39/28. Find the number of addresses in this block.
50
Computer Networks
Practice Questions